## Slide 1
PNR2 · ROBOTICS, DRONES & AUTONOMOUS SYSTEMS
SHADE
Ghost-aware decentralized task auction
A multi-robot task allocation protocol that keeps working when the network fails, and is honest about what that costs.
PROJECT PRESENTATION
Software-only · Python protocol core · ROS 2 + Gazebo simulation
Shadow-Hedged Auction with Decaying Estimates
Notes: SHADE stands for Shadow-Hedged Auction with Decaying Estimates. One line: robots allocate tasks among themselves, and when they lose contact with each other they reason about what the silent robots could be doing instead of just timing them out.

## Slide 2
01 · THE PROBLEM
One coordinator, one point of failure
PNR2 · SHADE protocol
2
Single point of failure
If the central allocator goes down, the whole fleet stops taking orders.
Unreliable links
Hazard zones cause dropouts and partitions that cut robots off from the hub.
Bottlenecks and stale plans
Every decision funnels through one node working from outdated robot state.
CENTRALIZED
SHADE
X
Hub down, fleet down
Any robot down, fleet continues
Notes: Centralized allocators are simple but fragile. In hazardous or remote environments links drop constantly, and a hub failure freezes every robot.

## Slide 3
02 · WHAT PNR2 REALLY ASKS
The hard part: deciding under silence
PNR2 · SHADE protocol
3
THREE THINGS PULL AGAINST EACH OTHER
Optimality
The task should go to the best robot, even one briefly out of range.
Latency and starvation
Every task should be claimed soon and never wait forever.
Duplicate work
Two partitions should not both do the same task for long.
THE USUAL ANSWERS EACH GIVE ONE UP
Claim immediately
Sub-optimal picks and duplicate work
Wait for a quorum
The smaller partition starves
Fixed timeout
Arbitrary; a better silent robot looks dead
SHADE: choose availability, put a price on the risk, bound it, repay it after the heal.
Notes: When robot R stops hearing robot P, R cannot tell whether P is dead, busy, or alive and better suited. Every existing answer sacrifices one of three things.

## Slide 4
03 · THE SOLUTION
SHADE in one slide: five ideas
PNR2 · SHADE protocol
4
1 Implicit bidding
Bids are computed from signed state manifests. No bid messages are sent.
2 Ghost bids
A silent robot still counts, as the best bid it could still be making.
3 Progress leases
A claim stays valid only while remaining cost visibly falls.
4 Witnessed state
Physics checks, neighbour sightings and equivocation proofs.
5 Finish-line rule
After a heal, the robot closer to done keeps the task.
Common thread: every decision is a pure function of signed, shared data, so robots agree without talking.
Notes: Each idea answers one requirement of the problem statement. Details follow on the next slides.

## Slide 5
04 · WALKTHROUGH
One task, start to finish
PNR2 · SHADE protocol
5
Six robots, R1 to R6. A network cut means R4 cannot hear R6.
1
Create
A task site issues T7; it gossips to every reachable robot.
2
Compute
Each robot evaluates everyone’s bid from manifests. R4 ranks first.
3
Check ghosts
R6 is silent for 3.1 s. Its best possible bid, 0.85, beats R4’s 0.55: regret 0.30.
4
Wait
Wait = P × regret / W = 5 × 0.30 / 1.3 ≈ 1.15 s. R6 stays silent, so R4 claims.
5
Hold a lease
R4 renews its claim only with a falling, physically possible remaining cost.
6
Fail
R4 stalls. The ratchet fails, the lease lapses, and R1 (rank 1) takes over.
7
Heal
The cut heals. R6 also worked on T7; the robot closer to done keeps it.
Every step is local computation over shared data. No coordinator, no vote.
Notes: Walk the audience through the life of task T7. Numbers use the default parameters: patience P = 5 s, bid range W = 1.3.

## Slide 6
05 · IMPLICIT BIDDING
Mechanism 1: a bid is a function, not a message
PNR2 · SHADE protocol
6
MANIFEST: SIGNED STATE EVERY ROBOT GOSSIPS
id
seq
timestamp
pose
velocity
battery
capabilities
lease
signature
B = G · (0.30·s_dist + 0.25·s_batt
+ 0.25·s_eta + 0.20·s_fit) − 0.3·σ
G
Gate: capable, battery covers trip plus reserve, finishes before the deadline.
σ
Uncertainty: pose noise, link quality, manifest age. Risky robots bid less.
=
Deterministic: shared map, Dijkstra distance fields, lowest-ID tie-break.
0
bid messages per task
TRANSMISSIONS PER NEW TASK (ESTIMATE)
Plain auction N(2 + h̄)
SHADE 2N
33–60% fewer, depending on average hop count h̄
Notes: Each robot gossips a signed manifest. Everyone runs the same public bid function on it, so anyone can compute anyone’s bid at any time.

## Slide 7
06 · THE CORE NOVELTY
Mechanism 2: ghost bids
PNR2 · SHADE protocol
7
R6
last heard 3.1 s ago
reachable set = v_max × age
T7
ghost bound 0.85
R4
R4 bid 0.55
regret = 0.85 − 0.55 = 0.30
GHOST UPPER BOUND
B_ghost = B(d − v_max·age, σ = 0)
REGRET
ρ = max(0, max B_ghost − B_mine)
TOLERANCE, GROWS WITH TASK AGE
ε = W · min(1, age / P)
CLAIM RULE
claim when ρ ≤ ε
Unlike a timeout, this asks per task: could this silent robot beat me here, and by how much?
Notes: The reachable set grows with silence. The ghost bid assumes the silent robot is as close to the task as its top speed allows, which is an upper bound on anything it could really bid.

## Slide 8
07 · REGRET-BOUNDED CLAIMING
Waiting in proportion to what could be lost
PNR2 · SHADE protocol
8
Chart: Tolerance vs task age (P = 5 s, W = 1.3)
| 0.0 | 0.5 | 1.0 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5 | 5.0 | 5.5 | 6.0
Tolerance ε | 0 | 0.13 | 0.26 | 0.39 | 0.52 | 0.65 | 0.78 | 0.91 | 1.04 | 1.17 | 1.3 | 1.3 | 1.3
Regret 0.30 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3
Regret 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05 | 0.05
≈ 1.15 s
wait at regret 0.30 (wait = P × ρ / W)
≈ 0.19 s
wait at regret 0.05
≤ P
after the patience window any robot may claim: starvation is bounded
Notes: The tolerance line rises with task age. A robot claims when the line crosses its regret, so a small regret costs almost no waiting and a large one costs about a second. After the patience window, any regret is accepted, which bounds starvation.

## Slide 9
08 · RECOVERY WITHOUT RE-AUCTION
Mechanisms 3 and 4: ranks and progress leases
PNR2 · SHADE protocol
9
SUCCESSION RANKS
Everyone computes the same ranked list. Rank i waits i × δ before claiming.
R4 rank 0
claims at once
R1 rank 1
+ 0.3 s
R2 rank 2
+ 0.6 s
When an owner fails, the next rank is already known. Recovery = lease lapse + i × δ, with no new auction round.
PROGRESS-RATCHET LEASE
A claim is renewed only by proof of progress.
Ratchet
remaining cost falls ≥ 0.5 s per second
Floor
remaining cost ≥ distance ÷ v_max + work left
A stalled robot reporting a constant cost fails the ratchet. One faking a falling cost breaks the floor. Peers catch it either way, without a vote.
Notes: Ranks remove the thundering herd and make recovery instant. Leases that need proof of progress catch robots that are alive but stuck or lying, which heartbeats cannot do.

## Slide 10
09 · BYZANTINE CONTAINMENT
Mechanism 5: containing faulty robots
PNR2 · SHADE protocol
10
Faulty robots hold valid keys but cannot forge signatures or beat physics. Three strikes quarantine a robot (60 s, doubling). No honest majority assumed.
Position liar
Kinematic check plus two witness sightings
Bid ignored, strike
Battery liar
Battery cannot rise or stay flat while working
Strike, then quarantine
Stall after claim
Progress ratchet and physical floor
One lease period lost
Equivocation
Two signed manifests with the same sequence number
Key banned fleet-wide
False DONE
Only the task site can sign a completion
Rejected, strike
Capability inflation
Capabilities must match the key registry
Rejected, strike
Task flood
Only authorised issuers may create tasks
Rejected, strike
Small unobserved lie
Stays inside the physical envelope
Bounded, not removed
Notes: We do not out-vote faulty robots. We limit what they can claim, make most lies self-evidently false, and bound the damage of the rest.

## Slide 11
10 · LEDGER AND FINISH-LINE RULE
Mechanism 6: merging after a partition
PNR2 · SHADE protocol
11
LEDGER: FOUR GROW-ONLY SETS
TASKS
CLAIMS
YIELDS
DONES
Merge = set union, so replicas converge after any partition, in any order, with duplicates.
FINISH-LINE YIELD RULE
A yields if c_B < c_A − m
or |c_B − c_A| ≤ m and id_B < id_A
c = remaining cost, m = hysteresis margin. Closer to done keeps the task.
LEMMA 1 · AT LEAST ONE OWNER CONTINUES
If honest remaining costs never rise, two honest contenders can never both yield.
Each robot judges the other from an older record, which can only overstate the other’s cost. Each of the four combinations of clauses leads to a contradiction, so no task is ever lost in a merge.
Notes: The ledger merges by set union, so it can never conflict. When two robots own the same task after a heal, the one closer to finishing keeps it, and we can prove no task is ever abandoned by both.

## Slide 12
11 · FORMAL GUARANTEES
What SHADE guarantees, and what it does not
PNR2 · SHADE protocol
12
G1
Convergence
Same records give the same task state on every robot.
G2
No lost task
Two honest contenders never both yield (Lemma 1).
G3
Bounded starvation
Claimed within P + (n−1)·δ + gossip delay.
G4
Bounded regret
Every claim’s regret is at most ε at claim time.
G5
Byzantine delay
At most one lease period per fault, then a strike.
G6
Bounded duplicates
Duplicate ownership ends soon after a heal.
G7
No deadlock
Every wait is a timer; nobody waits on a reply.
✗
Not promised
Exactly-once during a partition; global optimality; catching unobserved small lies.
Assumptions: bounded clock drift, unforgeable signatures, known speed and drain limits, fair-lossy links.
Notes: Seven bounded guarantees, each proven under stated assumptions. The eighth card is equally important: say clearly what is not promised.

## Slide 13
12 · ARCHITECTURE
System architecture
PNR2 · SHADE protocol
13
ROBOT AGENT · IDENTICAL ON EVERY ROBOT
same agent × N robots, linked by gossip
Publisher
signs manifests, sends on drift
Gate + Trust
6 checks, strikes, quarantine
Bid Evaluator
bid function, ghost upper bounds
Claim Manager
ranks, regret test, claims
Lease Monitor
ratchet and floor, expiry
Ledger Replica
grow-only sets, digests
Executor
moves, works, reports progress
Task Issuer
signed tasks, rate-limited
Gossip transport signed messages, multi-hop relay, real or emulated network
OBSERVER PLANE · READ-ONLY, NOT IN THE CONTROL PATH
Telemetry Tap
copies events out only
Telemetry API
FastAPI, WebSocket
Metrics Store
PostgreSQL, replay log
Dashboard
map, ghost halos, chaos lab
Notes: Every robot runs the same eight-module agent. The observer plane only listens through a one-way telemetry tap, so losing the dashboard never affects the fleet.

## Slide 14
13 · USER INTERFACE
Dashboard: making the protocol visible
PNR2 · SHADE protocol
14
MISSION CONTROL · Scenario: demo · t = 96 s
Cut
Kill
Liar
FLEET MAP
ghost
ROBOTS
R1
going
R2
working
R3
QUARANTINED
R4
ghost
AUCTION LOG
t=91.2 T7 open; ghost R6 regret 0.30
t=92.4 T7 -> R4 (waited 1.15 s)
t=95.0 R3 quarantined: lease stall
METRICS
Completion — %
Contested —
Regret —
1
1
Live map with ghost halos
Partitions, links and each silent robot’s reachable set.
2
2
Robot roster with trust
Battery, state, and quarantine status per robot.
3
3
Auction log with regret
Why each robot waited, claimed or yielded.
4
4
Live metrics and chaos
Cut the network, kill robots, inject liars.
Notes: The ghost halo is the visual signature of the project: the audience sees the bound, not just hears about it. The dashboard is observer-only.

## Slide 15
14 · COMPLEXITY
Complexity compared with existing approaches
PNR2 · SHADE protocol
15
Method | Messages per new task | Decision latency | Computation | Under partition
Centralized (Hungarian) | ≈ h̄ (fewest) | ≈ 2D hops + solve | O(n³) at the hub | Only the hub’s side works
Plain auction | N(2 + h̄) | ≈ 2D hops + bid window | O(T) per robot | Stalls if auctioneer is cut off
CBAA / CBBA | up to N × rounds, T entries each | rounds × round time | O(T × bundle) per round | Each side converges, slowly
Quorum (Raft / PBFT) | O(N) to O(N²) | several round trips | small | Minority side cannot decide
SHADE | 2N, zero bid messages | ≈ 1 tick + D hops | O(N × T) per robot per tick | Every side keeps allocating
N robots · T open tasks · D network diameter in hops · h̄ average hops between robots. Analytical estimates; the CBBA round count is a worst-case bound.
Notes: Read across the SHADE row. It removes bid messages and the bid round, and keeps working in every partition. The price is more local computation per robot, covered two slides later.

## Slide 16
15 · ESTIMATED REDUCTION
Worked example: how much SHADE reduces
PNR2 · SHADE protocol
16
Assumptions: 8 robots, 10 open tasks, 3-hop diameter, 2 hops average, 30 ms per hop, 0.5 s bid window.
50%
fewer transmissions per new task (32 to 16)
≈ 85%
faster decision (0.68 s to about 0.1 s)
∞ → 6.4 s
recovery from a robot that is alive but stalled
Quantity | Plain auction | CBBA (worst case) | SHADE
Transmissions per new task | 32 | ≈ 240 messages × 10 entries | 16
Time to decide (no ghosts) | ≈ 0.68 s | ≈ 3 s | ≈ 0.1 s
Crash recovery (same 6 s timeout) | ≈ 6.7 s | re-converge | ≈ 6.4 s
Stalled-but-alive robot | never recovered | never recovered | ≤ 6.4 s
Notes: These numbers come from the analytical model, not from measurements. Experiment E7 will confirm or correct them.

## Slide 17
16 · HONEST TRADE-OFFS
Where SHADE costs more, and the fix
PNR2 · SHADE protocol
17
Chart: Transmissions per second, 8 robots (model)
| 0.0 | 0.5 | 1.0 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0
Plain auction | 16 | 32 | 48 | 64 | 80 | 96 | 112 | 128 | 144
SHADE, full flooding | 64 | 72 | 80 | 88 | 96 | 104 | 112 | 120 | 128
SHADE, two-tier relay | 20.8 | 28.8 | 36.8 | 44.8 | 52.8 | 60.8 | 68.8 | 76.8 | 84.8
Background traffic
O(N² × f) relayed manifests. Fix: two-tier relay and a slower heartbeat while idle.
Local computation
O(N × T) bid evaluations per tick: trivial at 8 × 10, heavy at 100 × 100. Fix: rank only robots that can reach the task.
We say so
At the demo rate (0.12 tasks/s) SHADE sends more messages overall. The win is latency, recovery and availability.
Notes: Manifests are relayed fleet-wide, so background traffic grows with N squared. At the demo task rate SHADE sends more messages in total than a plain auction. Two-tier relay (full rate to neighbours, every fifth manifest beyond) moves the crossover from about 3 to about 0.3 tasks per second.

## Slide 18
17 · EVALUATION DESIGN
How we will measure it
PNR2 · SHADE protocol
18
METRICS
Completion before deadline
Mean regret vs full-state oracle
Time to claim (p50, p95)
Starved tasks
Duplicate robot-seconds
Energy per task
Heal convergence time
Messages per task
Byzantine cost before quarantine
BASELINES
Central oracle (perfect information)
Central allocator over the real network
Greedy nearest robot
Plain auction with timeouts
CBBA (Choi, Brunet, How, 2009)
ABLATIONS
No ghosts: always claim
Strict ghosts: always wait
No ratchet: heartbeat leases
No witnesses
Lowest-ID yield rule
No succession ranks
30 seeds per configuration · mean and 95% confidence interval · identical seeds across methods · scenario files published
Notes: Each ablation disables one mechanism. If removing it does not hurt a metric, the mechanism is not pulling its weight.

## Slide 19
18 · EXPERIMENT PLAN
Experiments
PNR2 · SHADE protocol
19
HYPOTHESES, NOT RESULTS
ID | Question | Sweep | Expected outcome
E1 | What does SHADE cost when nothing fails? | Healthy fleet | Close to the central oracle; more background messages
E2 | How does it degrade with packet loss? | Loss 0 to 80% | Completion holds longer than plain auction and central
E3 | What is the price of patience? | θ from 0.05 to 1.0 | Smooth regret vs latency curve; default near the knee
E4 | Which mechanism matters most? | Storm, all ablations | Each ablation loses on at least one metric
E5 | How fast does it recover from a heal? | 2 and 3 partitions | Contested tasks resolved within seconds
E6 | How much can faulty robots hurt? | 4 attack types | At most one lease period per strike
E7 | Does it scale? | 10 to 100 robots | Per-task cost flat; computation needs pruning
Notes: The right-hand column is what we expect, stated before we run anything, so the results can prove us wrong.

## Slide 20
19 · SIMULATION
Simulation: ROS 2 + Gazebo, plus a fast headless mode
PNR2 · SHADE protocol
20
IN DEVELOPMENT
Gazebo Harmonic world
arena, obstacles, 12 work sites, chargers, 8 diff-drive robots
ros_gz bridge
velocity commands, odometry, clock
8 SHADE agent nodes
one per robot, the real protocol code
Referee node
network emulator, fault injector, task sites, metrics
RViz overlay
tasks, links, cuts, ghost halos, claims
FLEET
Scout × 3
SENSE, 1.0 m/s
Hauler × 3
CARRY, 0.6 m/s
Generalist × 2
SENSE, CARRY, MANIPULATE, 0.8 m/s
SCENARIOS
Healthy
Lossy
Partition
Flapping
Crashes
Byzantine
Scale
Storm
Notes: The same Python agent runs inside ROS 2 nodes for the Gazebo demo and in a headless loop for 30-seed experiments. Status: in development.

## Slide 21
20 · DEMO SCRIPT
Seven-minute demo
PNR2 · SHADE protocol
21
Minute | Action | What the audience sees and learns
0–1 | Healthy run beside the central baseline | Similar completion: the protocol costs little when nothing fails
1–2 | Kill the central allocator | Central fleet freezes; SHADE fleet continues
2–3 | Cut the network into two groups | Ghost halos appear and grow: silence is quantified
3–4 | Create a task near a ghost | A robot waits about a second, then claims
4–5 | Inject a stall attacker | Its lease stops renewing; the next rank takes over
5–6 | Heal the network | Two owners of one task; the closer one keeps it
6–7 | Show the trade-off curve and ablations | Every mechanism is measured, including its costs
Notes: One idea per minute. End on the ghost halo shrinking as the silent robot comes back into range.

## Slide 22
21 · TECHNOLOGY
Tech stack
PNR2 · SHADE protocol
22
Robot agent
Python 3.11
asyncio
Ed25519 signatures
Dijkstra distance fields
Simulation
ROS 2 Jazzy
Gazebo Harmonic
ros_gz bridge
RViz2
Headless mode
Discrete-time simulator
Seeded scenarios
matplotlib viewer
Comms and ledger
UDP gossip
Network emulator
Logical clocks
G-Set ledger
Backend and data
FastAPI
WebSockets
PostgreSQL
Redis (Level 4)
Frontend
React
Vite
Canvas fleet map
Recharts
DevOps
Docker
GitHub Actions
Kubernetes
Prometheus + Grafana
Notes: Python keeps the protocol readable and testable. ROS 2 and Gazebo give a credible robot simulation. The web stack is only for the observer plane.

## Slide 23
22 · PLAN
Roadmap: Levels 1 to 4
PNR2 · SHADE protocol
23
1
LEVEL 1
Idea, architecture, planning
SRS and bid function
Architecture and data flow
UI wireframes
Stack and roadmap
Gate: design frozen
2
LEVEL 2
Core MVP
Agent: ghosts, ranks, leases
Ledger and finish-line rule
Simulator and Gazebo world
DB, APIs, 2D dashboard
Gate: scenarios run end to end
3
LEVEL 3
Intelligence, security, deployment
Witnesses, signatures, strikes
Learned ETA, tuned weights
Ablations E1–E7 in CI
Cloud deploy, 3D view
Gate: experiments and security pass
4
LEVEL 4
Scale and reliability
Kubernetes seed runners
Redis caching
Prometheus and Grafana alerts
100-robot load test
Gate: load test passes
Notes: Each level ends with something demonstrable. A level does not start until the previous gate passes.

## Slide 24
23 · POSITIONING
Related work and our honest claim
PNR2 · SHADE protocol
24
Work | What it does | How SHADE differs
FORMICA (2026) | Learns to predict teammates’ bids for communication-free allocation | Analytic upper bound from reachability, used as a claim guard; uses messages when they arrive
TGPR (preprint) | Link-reliability estimates; confidence-gated claims after a stalled award | No coordinator; wait derived from regret and task age, with a starvation bound
CBBA (2009) | Consensus on winning bids; conflict-free with a worst-case guarantee | No bid messages; acts before agreement; designed for partitions
Repeated auctions (Nanjanath, Gini) | Re-auctions remaining tasks after each completion | Recovery is precomputed through succession ranks
Sariel, Balch, Erdogan (2006) | Auctions robust to message loss and robot failure | Adds progress leases, a Byzantine model and proven bounds
Our claim: a new synthesis with proven bounds. Our literature check is short, so we will extend it before the final round.
Notes: Name the closest neighbours before the judges do. Our claim is a new combination with proven bounds, not "the first ever".

## Slide 25
24 · RISKS
Risks and how we handle them
PNR2 · SHADE protocol
25
Scope
Six mechanisms plus simulator and dashboard.
Build in layers; each layer demos alone.
Bid determinism
Different bids on different robots break agreement.
Shared map, deterministic Dijkstra, unit tests.
Loose ghost bound
Robots may wait for peers that could not help.
Exclude busy ghosts, drop after 60 s, cap by P.
Background traffic
Manifest relaying grows with N squared.
Two-tier relay and slower idle heartbeats.
Duplicate work
Both partitions may do one task.
Idempotent tasks; measured in every run.
Novelty challenge
Someone may have published something close.
Present as synthesis; extend literature check.
Notes: Most risks are about scope and tuning, not theory. The scope-cut order keeps the project’s identity intact if time runs short.

## Slide 26
No coordinator.
No single point of failure.
Silence has a price,
and we bound it.
Thank you · Questions?
Notes: Close on the tagline. Likely questions: Is this just CBBA? What about duplicate work? Can a malicious robot break it? Why not Raft? Answers are in the design doc, Section 15.